## Slide 1: Industrial Controls
Introduction

## Slide 2: Industrial controls
What are they? Where are they found?
Protective Relays
Building Automation Controllers
Programmable Logic Controllers
Communications Processors
Smart Controls
Data Trend Recorders
Process Controllers
Human Machine Interfaces and Displays

## Slide 3: How do we interact
Front Panel or Human Machine Interface
Direct interaction with device itself
Buttons/Switches/Screens/Etc.
Basic settings and some logic
Ethernet (RJ45) Network Communications
Direct or Network connection
Interaction through PC via software platform
Advanced settings and logic
Serial (EIA232 or EIA485) Communications
Direct device connection, minimal parameters
Interaction through PC via software platform
Moderate settings and logic

## Slide 4: Sel-351s Protection System
Relevant Software:
AcSELerator Quickset (SEL-5030)
TeraTerm Terminal Emulator
Settings and Configurations Methods:
Front Panel Control
Serial Communications
Ethernet Communications
Logic Capabilities:
Proprietary SELogic (3xx Series)
Primary Control Application:
Power Grid Protection
AC V/I Measurements
Digital Outputs

## Slide 5: Sel-849 motor management relay
Relevant Software:
AcSELerator Quickset (SEL-5030)
TeraTerm Terminal Emulator
Settings and Configurations Methods:
External HMI (SEL-3421/-3422)
Serial Communications
Ethernet Communications
Logic Capabilities:
Proprietary SELogic
Primary Control Application:
Medium Voltage Motor Protection
AC V/I Measurements
Digital Outputs
Arc Flash Protection

## Slide 6: Sel-35xx Real Time Automation controlLer
Relevant Software:
AcSELerator RTAC (SEL-5033)
Web Browser (Chrome/Firefox)
Settings and Configurations Methods:
Ethernet Communications
Logic Capabilities:
IEC 61131-3 Standard
  Ladder Diagrams
  Continuous Function Charts
  Structured Text
Primary Control Application:
Communications Aggregation
Power System SCADA
Data Collection/Aggregation
Logic/Automation Controller

## Slide 7: Productivity2000 Programmable logic controller
Relevant Software:
Productivity Suite
Settings and Configurations Methods:
Ethernet Communications
Logic Capabilities:
Ladder Diagrams
Primary Control Application:
Digital Inputs and Outputs
Data Collection/Aggregation
Logic/Automation Controller